## Slide 1
Digital Surveillance Solution HD Board install Guide
www.servntec.com

## Slide 2
<number>
HD-DVR Install
Install Express 16 Slot
Input PC Power
H.264 board
HD board
ITEM | model | remark
CPU | Intel® Core i5-750 Processor | 
Mother Board | Asus P7P55D-LE | 
VGA Card | ATI HD4350 256MB over | 
Memory | Non-ECC DDR3 DIMMs 2GB over | 
HDD | SATA 1TB 32MB over | 
OS | Windows 7 32bit (XP 지원) | 
System Specification
Board Install
Notes: <number>

## Slide 3
<number>
HD-DVR Install
Model |  | HDH-4812 | HDH-2412 | HDS-1204 | HDS-2408 | SDH-H4816 | SDH-H2408
Image | SDI Board |  |  |  |  |  | 
 | Analog Board (H.264) |  |  |  |  |  | 
Channels | HD-SDI | 4ch | 4ch | 4ch | 8ch |  | 
 | Analog | 16ch | 8ch | 0ch | 0ch | 16ch | 8ch
Display/Recording Frame (1080 30P) |  | 120/60 fps | 120/60 fps | 120/60fps | 240/120fps |  | 
Display/Recording Frame (720 60P) |  | 120/120fps | 120/120fps | 120/120fps | 120/120fps |  | 
Display/Recording Frame (D1) |  | 480/480 | 240/240 |  |  | 480/480 | 240/240
Specification
Notes: <number>

## Slide 4
<number>
Preparation before Program Installation
1. OS install (XP, Win7)
2. Driver Install (Mother b’d, VGA, etc)
3. Resolution Setup (1024X768 32bit)
4. disable Setup Screen Save
5. Install DVR board.
Please partition HDD on installing O/S. Uses can not make <IMAGEDB> in “C” driver, so can not save this in “C” driver
Recommend O/S size: More than 20GB
Notes: <number>

## Slide 5
<number>
Step 1 :
Driver Install
Step 2 :
Program Installation
Select Model
HD-SDI board driver
H.264 board driver
Select Language
When inserting CD(Installation CD), it starts automatically
Driver & Software Installation
Notes: <number>

## Slide 6
<number>
Step 3 :
Make <Image DB>
Select Drive
Select Image DB Size
Have to Restart System to apply
Driver & Software Installation
Notes: <number>

## Slide 7
<number>
Step 3 :
Make <Image DB>
Select Drive
Select Image DB Size
Have to Restart System to apply
Driver & Software Installation
Notes: <number>

## Slide 8
<number>
<N.B> Once Log-in, there is no automatic <Log-out>.
So please log-out after the operation
Default Account
ID: admin
Password: 1111
Virtual Keyboard
Login/Logout
Live display
Screen split
DVR OFF
Login
Data / Time information
Live Audio
Sensor/Relay
Information
Camera status
Color control
DVR Setup
Record image Search
PTZ control
Screen Split
Full Screen
Screen Change
Auto Rotation
Live View Overview
Logging In to DVR
DVR program start by automatically
DVR Start
Notes: <number>